## Slide 1
UV-VIS Spectroscopy

## Slide 2: What is UV-VIS Spectroscopy?
1
UV-VIS Spectroscopy:
Ultraviolet-visible spectroscopy or ultraviolet-visible spectrophotometry (UV-Vis or UV/Vis) refers to absorption spectroscopy or reflectance spectroscopy in the ultraviolet-visible spectral region.
Ultraviolet-visible (UV-VIS) spectroscopy is an analytical method that can measure the analyte quantity depending on the amount of light received by the analyte.
2
How it Works:
Concentration measurement using a UV-Vis-NIR spectrophotometer is guided by the Lambert-Beer Law. Asserting that the amount of light absorbed is directly proportional to the concentration of solute in the solution and path length under analysis, the Lambert-Beer Law underpins the spectroscopy and has been indispensable in interpreting spectroscopic data.
Key components of UV-Vis-NIR spectrophotometers include the light source, such as deuterium lamps (UV) or tungsten-halogen lamps (Vis-NIR), the monochromator, which disperses light into its component wavelengths; and the detector, which converts transmitted or reflected light into measurable data. A wide variety of sample holders are available to measure a variety of samples.

## Slide 3
Ultraviolet-Visible Spectrophotometer
Ultraviolet/Visible area (UV-Vis) measurements span wavelengths from around 200 nm to 800 nm. The absorption by a molecule of ultraviolet or visible radiation results in transitions between the molecule’s electrical energy levels. The optical and electronic properties of different materials, such as films, powders, monolithic solids, and liquids, are suitable for characterization.
UV-vis spectroscopy is a cost-effective, simple, versatile, non-destructive, analytical technique suitable for a large spectrum of organic compounds and some inorganic species. As a function of wavelength, UV-vis spectrophotometers measure the absorption or transmission of light that passes through a medium.
In order to classify and measure the concentration of substances in liquid streams, high performance liquid chromatography and ultra-high performance liquid chromatography incorporate UV-vis detectors. It allows the detection of all animals by integrating these techniques with mass spectrometry.
Notes: When conducting research, it is easy to go to one source: Wikipedia. However, you need to include a variety of sources in your research. Consider the following sources:
Who can I interview to get more information on the topic?
Is the topic current and will it be relevant to my audience?
What articles, blogs, and magazines may have something related to my topic?
Is there a YouTube video on the topic? If so, what is it about?
What images can I find related to the topic?

## Slide 4
UV-VIS Spectroscopy Theory
When the interaction between incident radiation and the electron cloud in a chromophore results in an electronic transition involving the promotion of one or more of the outer shell or the bonding electrons from a ground state into a higher energy state, ultraviolet-visible (UV-Vis) spectra are derived.
Generally, the UV and visible spectral bands of substances are large. And may not exhibit a high degree of compound recognition accuracy. Nonetheless, they are sufficient for quantitative assays and are useful as an alternate means of detection for several substances. The radiation from typical hot solids consists of several wavelengths and depends primarily on the temperature of the solid and is predictable from the principle of chance, the energy released at each given wavelength.
More recently, using a version of this-the tungsten-halogen lamp-has become standard practice. Radiation is transmitted deep into the UV zone through the quartz envelope. The most popular source is the deuterium lamp for the UV region itself, and a UV-Visible spectrometer would normally have all types of lamps to fill the whole wavelength spectrum.
Notes: Once you find your sources, you will want to evaluate your sources using the following questions:
Author:
Who is the author?
Why should I believe what he or she has to say on the topic?
Is the author seen as an expert on the topic? How do you know?
Current:
How current is the information in the source?
When was the source published?
Is the information out-of-date?
Accuracy:
Is the content accurate?
Is the information presented objectively? Do they share the pros and cons?

## Slide 5
Applications of UV-VIS Spectroscopy
In research, ultraviolet/visible spectroscopy is used more commonly than in detection. Through first reacting the sample to bring the metal into solution as an ion, the trace metal content of an alloy, such as manganese in steel, can be determined.
A common technique for quantitative analysis of analytes in QA/QC, analytical research, and government regulatory laboratories is UV-Visible spectrophotometry. The fundamentals of the approach are learned in school, such as Beer’s Law. UV-Visible Mid-range to Upper-end Spectrophotometers are typically used in research laboratories, including university and industrial laboratories.
The ion is then complexed or made to react so that it can be measured in a shape, such as manganese as the manganate(VII) ion. When the spectrum is registered, the absorbance is the most valuable bit of information since the concentration of the solution can be determined if the absorption coefficient of the chromophore is known and thus the mass of the metal in the sample.
Notes: After consulting a variety of sources, you will need to narrow your topic. For example, the topic of internet safety is huge, but you could narrow that topic to include internet safety in regards to social media apps that teenagers are using heavily. A topic like that is more specific and will be relevant to your peers. Some questions to think about to help you narrow your topic:
What topics of the research interest me the most?
What topics of the research will interest my audience the most?
What topics will the audience find more engaging? Shocking? Inspiring?

## Slide 6
INSTRUMENTATION:
Instruments for measuring the absorption of U.V. or visible radiation are made up of the following components;
Sources (UV and visible)
filter or monochromator
Sample containers or sample cells
Detector
Notes: Now, that you have narrowed your topic, you will want to organize your research in a structure that works. There are some common organizational patterns based on the kind of research you are doing.
Organizational Structures:
Cause and Effect- this kind of structure is great for explaining the causes and effects of a topic
Compare and Contrast- in this pattern you highlight the similarities and differences of the topic
Explain process- this structure is great for outlining a series of steps to follow;
Definition- if you want to make sure your audience understands what something is using illustrations, meanings, clarifying misconceptions, you may want to use this structure
Classification- a common organizational structure is grouping like topics or facts from the research together. For instance, in the internet safety about social media apps, you may organize the research where you look at each social media app one at a time

## Slide 7
Radiation source:
It is important that the power of the radiation source does not change abruptly over its wavelength range.
The electrical excitation of deuterium or hydrogen at low pressure produces a continuous UV spectrum.
The mechanism for this involves formation of an excited molecular species, which breaks up to give two atomic species and an ultraviolet photon Both Deuterium and Hydrogen lamps emit radiation in the range 160 - 375 nm.
Quartz windows must be used in these lamps, and quartz cuvettes must be used, because glass absorbs radiation of wavelengths less than 350 nm.
Various UV radiation sources are as follows
a. Deuterium lamp
b. Hydrogen lamp
c. Tungsten lamp
d. Xenon discharge lamp
e. Mercury arc lamp
Various Visible radiation sources are as follows
a. Tungsten lamp
b. Mercury vapour lamp
c. Carbonone lamp
Notes: After you’ve done your research, it’s time to put your presentation together. The first step in the process is to introduce the topic. This is a great time to connect your topic to something that your audience can relate. In other words, why should they listen to all the information you will be sharing in your research presentation? What is in it for them? You may also want to include a graphic or image to grab their attention.
Feel free to duplicate this slide by right-clicking on this slide in the slides pane to the left and select Duplicate Slide.
The next step in your presentation is to state your claim or topic clearly. Your teacher may even call this your thesis. As you state your thesis, you may find that this layout is not the best layout for your claim or topic. You can change the layout by clicking the drop-down menu next to the Layout in the Slides menu section. You can choose Two Content, Comparison, or Picture with Caption. Note: A different layout might change the look of the icons on this page.
You will also want to state your facts. You have done the research now share some of the interesting facts with your audience. Facts do not have to be boring; you can communicate facts in a variety of ways by going to the Insert Tab. In the Insert tab you can:
Insert pictures from your computer or online.
Add a chart
Create some SmartArt
Insert a variety of icons to help your facts come to life. Note: You can change the color of the icons by selecting the icon and then click on the Format tab and then Graphics Fill. From there, you will choose a color from the list or choose More Fill Colors to give you more options.
Since this research presentation is a result of your hard work and searching, you want to make sure you support the claims or points in your presentation with facts from your research findings. Make sure you give the author proper credit for helping you share your ideas. If one of your sources has a video that is relevant to your topic, you can add the video as added support. Keep in mind the length of the video and the amount of time you have for your presentation. For a 5 minute speech, the video should be no longer than 30 seconds.
Questions to consider:
How will you state the author of the source?
Will you need to cite the source on the slide?
What are some ways you can engage your audience so they feel like they are a part of the presentation? Some ideas to consider is by taking a quick poll like: by a show of hands, how many of you think school uniforms are a way to cut down on bullying? Another suggestion is to have them hold up a certain number of fingers to see if they agree or disagree. Finally, you can share a story that the audience can relate to that makes them laugh.
After all the applause, your audience may have some questions. Be prepared to answer some of their questions by making a list of questions you think they might ask. You may also want to share the presentation with them by providing the link to your presentation, if they want more information.

## Slide 8
2. filters or monochromators:
All monochromators contain the following component parts;
• An entrance slit
• A collimating lens
• A dispersing device (a prism or a grating) 8
• A focusing lens
• An exit slit
Polychromatic radiation (radiation of more than one wavelength) enters the monochromator through the entrance slit. The beam is collimated, and then strikes the dispersing element at an angle.
The beam is split into its component wavelengths by the grating or prism. By moving the dispersing element or the exit slit, radiation of only a particular wavelength leaves the monochromator through the exit slit.
Notes: After you’ve done your research, it’s time to put your presentation together. The first step in the process is to introduce the topic. This is a great time to connect your topic to something that your audience can relate. In other words, why should they listen to all the information you will be sharing in your research presentation? What is in it for them? You may also want to include a graphic or image to grab their attention.
Feel free to duplicate this slide by right-clicking on this slide in the slides pane to the left and select Duplicate Slide.
The next step in your presentation is to state your claim or topic clearly. Your teacher may even call this your thesis. As you state your thesis, you may find that this layout is not the best layout for your claim or topic. You can change the layout by clicking the drop-down menu next to the Layout in the Slides menu section. You can choose Two Content, Comparison, or Picture with Caption. Note: A different layout might change the look of the icons on this page.
You will also want to state your facts. You have done the research now share some of the interesting facts with your audience. Facts do not have to be boring; you can communicate facts in a variety of ways by going to the Insert Tab. In the Insert tab you can:
Insert pictures from your computer or online.
Add a chart
Create some SmartArt
Insert a variety of icons to help your facts come to life. Note: You can change the color of the icons by selecting the icon and then click on the Format tab and then Graphics Fill. From there, you will choose a color from the list or choose More Fill Colors to give you more options.
Since this research presentation is a result of your hard work and searching, you want to make sure you support the claims or points in your presentation with facts from your research findings. Make sure you give the author proper credit for helping you share your ideas. If one of your sources has a video that is relevant to your topic, you can add the video as added support. Keep in mind the length of the video and the amount of time you have for your presentation. For a 5 minute speech, the video should be no longer than 30 seconds.
Questions to consider:
How will you state the author of the source?
Will you need to cite the source on the slide?
What are some ways you can engage your audience so they feel like they are a part of the presentation? Some ideas to consider is by taking a quick poll like: by a show of hands, how many of you think school uniforms are a way to cut down on bullying? Another suggestion is to have them hold up a certain number of fingers to see if they agree or disagree. Finally, you can share a story that the audience can relate to that makes them laugh.
After all the applause, your audience may have some questions. Be prepared to answer some of their questions by making a list of questions you think they might ask. You may also want to share the presentation with them by providing the link to your presentation, if they want more information.

## Slide 9
3. sample containers or sample cells:
A variety of sample cells available for UV region. The choice of sample cell is based on
a) the path length, shape, size
b) the transmission characteristics at the desired wavelength
c) the relative expense
The cell holding the sample should be transparent to the wavelength region to be recorded.
Quartz or fused silica cuvettes are required for spectroscopy in the UV region. Silicate glasses can be used for the manufacture of cuvettes for use between 350 and 2000 nm.
The thickness of the cell is generally 1 cm. cells may be rectangular in shape or cylindrical with flat ends.
Notes: After you’ve done your research, it’s time to put your presentation together. The first step in the process is to introduce the topic. This is a great time to connect your topic to something that your audience can relate. In other words, why should they listen to all the information you will be sharing in your research presentation? What is in it for them? You may also want to include a graphic or image to grab their attention.
Feel free to duplicate this slide by right-clicking on this slide in the slides pane to the left and select Duplicate Slide.
The next step in your presentation is to state your claim or topic clearly. Your teacher may even call this your thesis. As you state your thesis, you may find that this layout is not the best layout for your claim or topic. You can change the layout by clicking the drop-down menu next to the Layout in the Slides menu section. You can choose Two Content, Comparison, or Picture with Caption. Note: A different layout might change the look of the icons on this page.
You will also want to state your facts. You have done the research now share some of the interesting facts with your audience. Facts do not have to be boring; you can communicate facts in a variety of ways by going to the Insert Tab. In the Insert tab you can:
Insert pictures from your computer or online.
Add a chart
Create some SmartArt
Insert a variety of icons to help your facts come to life. Note: You can change the color of the icons by selecting the icon and then click on the Format tab and then Graphics Fill. From there, you will choose a color from the list or choose More Fill Colors to give you more options.
Since this research presentation is a result of your hard work and searching, you want to make sure you support the claims or points in your presentation with facts from your research findings. Make sure you give the author proper credit for helping you share your ideas. If one of your sources has a video that is relevant to your topic, you can add the video as added support. Keep in mind the length of the video and the amount of time you have for your presentation. For a 5 minute speech, the video should be no longer than 30 seconds.
Questions to consider:
How will you state the author of the source?
Will you need to cite the source on the slide?
What are some ways you can engage your audience so they feel like they are a part of the presentation? Some ideas to consider is by taking a quick poll like: by a show of hands, how many of you think school uniforms are a way to cut down on bullying? Another suggestion is to have them hold up a certain number of fingers to see if they agree or disagree. Finally, you can share a story that the audience can relate to that makes them laugh.
After all the applause, your audience may have some questions. Be prepared to answer some of their questions by making a list of questions you think they might ask. You may also want to share the presentation with them by providing the link to your presentation, if they want more information.

## Slide 10
4. Detectors:
In order to detect radiation, three types of photosensitive devices are
a. Photovoltaic cells or barrier- layer cell
b. phototubes or photo emissive tubes
c. photomultiplier tubes
a. Photovoltaic cell is also known as barrier layer or photronic cell.
It consists of a metallic base plate like iron or aluminium which acts as one electrode. On its surface, a thin layer of a semiconductor metal like selenium is deposited.
Then the surface of selenium is covered by a very thin layer of silver or gold which acts as a second collector tube.
When the radiation is incident upon the surface of selenium, electrons are generated at the selenium- silver surface and the electrons are collected by the silver.
This accumulation at the silver surface creates an electric voltage difference between the silver surface and the basis of the cell. Phototubes are also known as photo emissive cells.
Notes: After you’ve done your research, it’s time to put your presentation together. The first step in the process is to introduce the topic. This is a great time to connect your topic to something that your audience can relate. In other words, why should they listen to all the information you will be sharing in your research presentation? What is in it for them? You may also want to include a graphic or image to grab their attention.
Feel free to duplicate this slide by right-clicking on this slide in the slides pane to the left and select Duplicate Slide.
The next step in your presentation is to state your claim or topic clearly. Your teacher may even call this your thesis. As you state your thesis, you may find that this layout is not the best layout for your claim or topic. You can change the layout by clicking the drop-down menu next to the Layout in the Slides menu section. You can choose Two Content, Comparison, or Picture with Caption. Note: A different layout might change the look of the icons on this page.
You will also want to state your facts. You have done the research now share some of the interesting facts with your audience. Facts do not have to be boring; you can communicate facts in a variety of ways by going to the Insert Tab. In the Insert tab you can:
Insert pictures from your computer or online.
Add a chart
Create some SmartArt
Insert a variety of icons to help your facts come to life. Note: You can change the color of the icons by selecting the icon and then click on the Format tab and then Graphics Fill. From there, you will choose a color from the list or choose More Fill Colors to give you more options.
Since this research presentation is a result of your hard work and searching, you want to make sure you support the claims or points in your presentation with facts from your research findings. Make sure you give the author proper credit for helping you share your ideas. If one of your sources has a video that is relevant to your topic, you can add the video as added support. Keep in mind the length of the video and the amount of time you have for your presentation. For a 5 minute speech, the video should be no longer than 30 seconds.
Questions to consider:
How will you state the author of the source?
Will you need to cite the source on the slide?
What are some ways you can engage your audience so they feel like they are a part of the presentation? Some ideas to consider is by taking a quick poll like: by a show of hands, how many of you think school uniforms are a way to cut down on bullying? Another suggestion is to have them hold up a certain number of fingers to see if they agree or disagree. Finally, you can share a story that the audience can relate to that makes them laugh.
After all the applause, your audience may have some questions. Be prepared to answer some of their questions by making a list of questions you think they might ask. You may also want to share the presentation with them by providing the link to your presentation, if they want more information.

## Slide 11
A phototube consists of an evacuated glass bulb.
There is light sensitive cathode inside it.
The inner surface of cathode is coated with light sensitive layer such as potassium oxide and silver oxide.
When radiation is incident upon a cathode, photoelectrons are emitted. These are collected by an anode.
Then these are returned via external circuit. And by this process current is amplified and recorded.
The photomultiplier tube is a commonly used detector in UV spectroscopy.
It consists of a photo emissive cathode (a cathode which emits electrons when struck by photons of radiation), several dynodes (which emit several electrons for each electron striking them) and an anode.
A photon of radiation entering the tube strikes the cathode, causing the emission of several electrons. These electrons are accelerated towards the first dynode (which is 90V more positive than the cathode).
The electrons strike the first dynode, causing the emission of several electrons for each incident electron.
These electrons are then accelerated towards the second dynode, to produce more electrons which are accelerated towards dynode three and so on.
Eventually, the electrons are collected at the anode. By this time, each original photon has produced 106 - 107 electrons. The resulting current is amplified and measured.
Photomultipliers are very sensitive to UV and visible radiation.
They have fast response times. Intense light damages photomultipliers; they are limited to measuring low power radiation.

## Slide 12
Single beam spectrophotometer is an analytical instrument in which all the light waves coming from the light source passes through the sample.
Therefore, the measurements are taken as the intensity of light before and after the light pass through the sample. These single beam spectrophotometers are more compact and optically simpler than double beam spectrophotometers. And also these instruments are less expensive.
Single Beam Spectrophotometer:
The sensitivity of detection of the light beam after it passes through the sample is high since it uses a non-split light beam (therefore, high energy exists throughout). Single beam spectrophotometers are available in analysis at visible and ultraviolet wavelength ranges.
A single beam spectrophotometer measures the concentration of an analyte in a sample by measuring the amount of light absorbed by that analyte. Here, the Beer Lambert Law comes into operation. This law states that the concentration of an analyte is directly proportional to the absorbance.
Notes: After you’ve done your research, it’s time to put your presentation together. The first step in the process is to introduce the topic. This is a great time to connect your topic to something that your audience can relate. In other words, why should they listen to all the information you will be sharing in your research presentation? What is in it for them? You may also want to include a graphic or image to grab their attention.
Feel free to duplicate this slide by right-clicking on this slide in the slides pane to the left and select Duplicate Slide.
The next step in your presentation is to state your claim or topic clearly. Your teacher may even call this your thesis. As you state your thesis, you may find that this layout is not the best layout for your claim or topic. You can change the layout by clicking the drop-down menu next to the Layout in the Slides menu section. You can choose Two Content, Comparison, or Picture with Caption. Note: A different layout might change the look of the icons on this page.
You will also want to state your facts. You have done the research now share some of the interesting facts with your audience. Facts do not have to be boring; you can communicate facts in a variety of ways by going to the Insert Tab. In the Insert tab you can:
Insert pictures from your computer or online.
Add a chart
Create some SmartArt
Insert a variety of icons to help your facts come to life. Note: You can change the color of the icons by selecting the icon and then click on the Format tab and then Graphics Fill. From there, you will choose a color from the list or choose More Fill Colors to give you more options.
Since this research presentation is a result of your hard work and searching, you want to make sure you support the claims or points in your presentation with facts from your research findings. Make sure you give the author proper credit for helping you share your ideas. If one of your sources has a video that is relevant to your topic, you can add the video as added support. Keep in mind the length of the video and the amount of time you have for your presentation. For a 5 minute speech, the video should be no longer than 30 seconds.
Questions to consider:
How will you state the author of the source?
Will you need to cite the source on the slide?
What are some ways you can engage your audience so they feel like they are a part of the presentation? Some ideas to consider is by taking a quick poll like: by a show of hands, how many of you think school uniforms are a way to cut down on bullying? Another suggestion is to have them hold up a certain number of fingers to see if they agree or disagree. Finally, you can share a story that the audience can relate to that makes them laugh.
After all the applause, your audience may have some questions. Be prepared to answer some of their questions by making a list of questions you think they might ask. You may also want to share the presentation with them by providing the link to your presentation, if they want more information.

## Slide 13
Double Beam Spectrophotometer:
Double beam spectrophotometer is an analytical instrument in which the light beam coming from the light source splits into two fractions.
One fraction acts as the reference (the reference beam) while the other fraction passes through the sample (sample beam). As a result, the reference beam does not pass through the sample.
The sample beam can measure the absorbance of the sample. The reference beam can measure the absorption (the sample beam can be compared with the reference beam). Therefore, the absorption is the ratio between the sample beam (after passing through the sample) and a reference beam.
A spectrophotometer has a monochromator that isolates the desired wavelengths from a light beam. The reference beam and sample beam recombine before moving to the monochromator. Consequently, this avoids or compensate the electronic and mechanical effects on both sample and reference beams, equally.
Notes: After you’ve done your research, it’s time to put your presentation together. The first step in the process is to introduce the topic. This is a great time to connect your topic to something that your audience can relate. In other words, why should they listen to all the information you will be sharing in your research presentation? What is in it for them? You may also want to include a graphic or image to grab their attention.
Feel free to duplicate this slide by right-clicking on this slide in the slides pane to the left and select Duplicate Slide.
The next step in your presentation is to state your claim or topic clearly. Your teacher may even call this your thesis. As you state your thesis, you may find that this layout is not the best layout for your claim or topic. You can change the layout by clicking the drop-down menu next to the Layout in the Slides menu section. You can choose Two Content, Comparison, or Picture with Caption. Note: A different layout might change the look of the icons on this page.
You will also want to state your facts. You have done the research now share some of the interesting facts with your audience. Facts do not have to be boring; you can communicate facts in a variety of ways by going to the Insert Tab. In the Insert tab you can:
Insert pictures from your computer or online.
Add a chart
Create some SmartArt
Insert a variety of icons to help your facts come to life. Note: You can change the color of the icons by selecting the icon and then click on the Format tab and then Graphics Fill. From there, you will choose a color from the list or choose More Fill Colors to give you more options.
Since this research presentation is a result of your hard work and searching, you want to make sure you support the claims or points in your presentation with facts from your research findings. Make sure you give the author proper credit for helping you share your ideas. If one of your sources has a video that is relevant to your topic, you can add the video as added support. Keep in mind the length of the video and the amount of time you have for your presentation. For a 5 minute speech, the video should be no longer than 30 seconds.
Questions to consider:
How will you state the author of the source?
Will you need to cite the source on the slide?
What are some ways you can engage your audience so they feel like they are a part of the presentation? Some ideas to consider is by taking a quick poll like: by a show of hands, how many of you think school uniforms are a way to cut down on bullying? Another suggestion is to have them hold up a certain number of fingers to see if they agree or disagree. Finally, you can share a story that the audience can relate to that makes them laugh.
After all the applause, your audience may have some questions. Be prepared to answer some of their questions by making a list of questions you think they might ask. You may also want to share the presentation with them by providing the link to your presentation, if they want more information.

## Slide 14
Applications:
1. Detection of Impurities
It is one of the best methods for determination of impurities in organic molecules.
Additional peaks can be observed due to impurities in the sample and it can be compared with that of standard raw material.
By also measuring the absorbance at specific wavelength, the impurities can be detected.
2. Structure elucidation of organic compounds
It is useful in the structure elucidation of organic molecules, such as in detecting the presence or absence of unsaturation, the presence of hetero atoms.
3. UV absorption spectroscopy can be used for the quantitative determination of compounds that absorb UV radiation.
4. UV absorption spectroscopy can characterize those types of compounds which absorbs UV radiation thus used in qualitative determination of compounds. Identification is done by comparing the absorption spectrum with the spectra of known compounds.
5. This technique is used to detect the presence or absence of functional group in the compound. Absence of a band at particular wavelength regarded as an evidence for absence of particular group.
6. Kinetics of reaction can also be studied using UV spectroscopy. The UV radiation is passed through the reaction cell and the absorbance changes can be observed.
7. Many drugs are either in the form of raw material or in the form of formulation. They can be assayed by making a suitable solution of the drug in a solvent and measuring the absorbance at specific wavelength.
8. Molecular weights of compounds can be measured spectrophotometrically by preparing the suitable derivatives of these compounds.
9. UV spectrophotometer may be used as a detector for HPLC.

## Slide 15: THANK YOU
Notes: You can use this slide as your opening or closing slide. Should you choose to use it as a closing, make sure you review the main points of your presentation. One creative way to do that is by adding animations to the various graphics on a slide. This slide has 4 different graphics, and, when you view the slideshow, you will see that you can click to reveal the next graphic. Similarly, as you review the main topics in your presentation, you may want each point to show up when you are addressing that topic.
Add animation to images and graphics:
Select your image or graphic.
Click on the Animations tab.
Choose from the options. The animation for this slide is “Split”. The drop-down menu in the Animation section gives even more animations you can use.
If you have multiple graphics or images, you will see a number appear next to it that notes the order of the animations.
Note: You will want to choose the animations carefully. You do not want to make your audience dizzy from your presentation.